JukCPU
Mini instruction set
Datasheet
JukCPU MiniISA is an 4 instruction cpu. The instructions have been optimized to:
- Have Extra Commands (Arthmeritic operations, subroutines)
- Handle basic I/O
- Have operations on almost only memory adresses
Go to next pages to see more about the optimized instructions, and to learn some code or to go use the prewritten (wozmon-like) os.

Have Fun!!!

Made by JulSM
1. Instruction set
With an 2 bit instruction set, it is really hard to fit basic commands in. That is why we have optimized the instruction set.

Instructions:
00 – Clone an memory adress. Can be very useful in io operations.
    Example usage (for io latch):
0x0 ; io to be latched
0x1 cmp 0x4 0x5 ; compare the io adrress to see if its null
0x2 copy 0x5 0x0 ; copy the io value to 0x0 and latch it
0x3 jmp 0x1 ; make an loop
0x4 0x0 ; null value (io idle or previous value)
0x5 ; io input
   Example useage (for screen):
0x0 0xf ; black color for screen
0x1 copy 0x0 0x3
0x2 jmp 0x1 ; make an loop for the screnn to go fully black
0x3 ; connected screen
- 01 addr – Jump to an memory adress (content of adress adrr)
- 10 – Compare two values. If output is true then jump 1, if false, jump 2
  Example usage:
  0x0 ; value 1
  0x1 ; value 2
  0x3 cmp 0x0 0x1 ; compare the 2 adresses
  0x4 jmp 0xf ; for if output is true
  0x5 ; normal code continues
  …
  0xf ; code for true comparison
- 11 – Extra commands determined by cmd bus after 1 clock cycle (00 addr1 addr2 adrr3 – add addr1 addr2 together and store them at addr3, 01 the same as add but with subtraction, 10 jsub jump to subroutine, 11 return from subroutine)

Example Wozmon-Like code
adress 0xfffc – clock for input
adress 0xfffd – input
adress 0xfffe – TTY clock
adress 0xffff – TTY
Code:
ROM
0x0000 copy 0x0001 0x0002 ; Copy value from address 0x0001 to 0x0002
0x0003 jmp 0x0010 ; Jump to address 0x0010
0x0006 cmp 0x0004 0x0005 ; Compare values at addresses 0x0004 and 0x0005
0x0009 add 0x0007 0x0008 ; Add values from addresses 0x0007 and 0x0008
0x000C sub 0x000A 0x000B ; Subtract value at address 0x000B from address 0x000A
0x000F jsub 0x0015 ; Jump to subroutine at address 0x0015
0x0012 ret ; Return from subroutine

; Print value at address 0xFFFF to TTY
0x0015:
    load R0, 0xFFFF ; Load the value from memory address 0xFFFF into register R0
    tty R0 ; Output the value from R0 to the TTY
    ret ; Return from subroutine

; Read keyboard input and store in address 0xFFFE
0x0018:
    keyboard ; Call a function or routine to read keyboard input
    store 0xFFFE, R0 ; Store the keyboard input (from register R0) in memory address 0xFFFE
    ret ; Return from subroutine
RAM:
0x0000: ; TTY output buffer
0x0001: ; Keyboard input buffer
0x0002: ; Scratch register or temporary storage
0x0003: ; Reserved or future use
0x0004: 0x0000 ; Variable 1
0x0005: 0x0001 ; Variable 2
0x0006: ; Reserved or future use
0x0007: 0x0005 ; Variable 3
0x0008: 0x0003 ; Variable 4
0x0009: ; Reserved or future use
0x000A: 0x0008 ; Result storage for subtraction
0x000B: 0x0002 ; Operand for subtraction
0x000C: ; Reserved or future use
0x000D: ; Reserved or future use
0x000E: ; Reserved or future use
0x000F: ; Reserved or future use
0x0010: ; Reserved or future use
0x0011: ; Reserved or future use
0x0012: ; Reserved or future use
0x0013: ; Reserved or future use
0x0014: ; Reserved or future use

Pinout
Pins 0-15: RAM adresses
Pins 16-32: Command Adress
Pins 33-34: Command
Pins 35-51: Data
Pin 52: 5V
Pin 53: GND
Pin 54: Reset